## Slide 1: ARM Instruction Set

## Slide 2: ARM Instruction Set
Instructions process data held in registers and access memory with load and store instructions.
Classification of instructions
Data processing instructions
Data Transfer Instructions - Load-Store instructions
Control flow instructions – Conditional & Branching instructions
S/W interrupt instructions
Program status register instructions

## Slide 3: 1. Data Processing Instructions
Perform arithmetic, logical, move, compare and multiply operations
All operations except multiply instructions are carried out in ALU
Uses 3- address instruction format:
  Eg: ADD R0,R1,R2 ; R0 = R1+R2
All operands are 32 bits wide.
  From register.
  Specified as literals in instruction itself.
Result is 32 bits wide
  Stored in register file.
Most Data Processing instructions can Pre-process one operand
using barrel shifter.
Eg: ADD R0,R1,R2, LSL #2 ; R2 = LSL by 2 position
; R0 = R1+R2

## Slide 4: 1. Data processing
Manipulate data within register
1.1 Arithmetic instructions
1.2 Logical instructions
1.3 Move instructions
1.4 Comparison instruction

## Slide 5: 1.1 Arithmetic Instructions
ADD r0,r1,r2
ADC r0,r1,r2
SUB r0,r1,r2
SBC r0,r1,r2
RSB r0,r1,r2
RSC r0,r1,r2
ADD add
ADC add with carry
SUB subtract
SBC subtract with carry
RSB reverse subtract
RSC reverse subtract with carry
Carry-in is the current value of C bit in CPSR

## Slide 7: 1.2 Bit-wise logical operations
AND r0,r1,r2
ORR r0,r1,r2
EOR r0,r1,r2
BIC r0,r1,r2
BIC
  Bit Clear
  Every ‘1’ in the second operand clears the corresponding bit in the first.

## Slide 9: 1.3 Register- Register movement operations
MOV Rd, N
Rd :destination register
N: can be an immediate value or source register
Example: MOV r7,r5
MVN Rd, N
Move into Rd negated value of the 32 bit value from source (N’).
Example: MVN r7,r5

## Slide 11: 1.4 Comparison
Enables comparison of 32 bit values
  Updates CPSR flags but do not affect other registers
CMP r1,r2 compare
CMN r1,r2 compare negated

## Slide 15: ADD r3,r2,r1, LSL #3
Single instruction.
Second reg operand subjected to shift.
LSL : Logical Shift Left.
Various shift & rotate operations:
  Logical Shift Left (LSL),
  Logical Shift Right (LSR),
  Arithmetic Shift Left (ASL),
  Arithmetic Shift Right (ASR),
  Rotate Right (ROR),
  Rotate Right Extended (RRX)
Shifted Register Operands

## Slide 17: With Barrel shifter
Use of Barrel shifter with arithmetic and logical instructions increases the set of possible available operations.
  Useful for fast multiplication and dealing with lists, table and other complex data structure.

## Slide 20: Multiply instructions
Multiply contents of a pair of registers
  Multiplication by immediate constants not supported.
- long multiply generates 64 bit result
Examples:
 mul r0,r1,r2
Contents of r1 and r2 multiplied and the result is put in r0.
umull r0,r1,r2,r3 ; unsigned multiply long
Unsigned multiplication with result stored in r0 and r1.
Number of cycles taken for execution of multiplication instruction depends upon processor implementation.

## Slide 22: Multiply and Accumulate
Result of multiplication can be accumulated with content of another register
MLA Rd, Rn, Rm, Racc
Rd = (Rn*Rm)+Racc
UMLAL RdLo, RdHi, Rn, Rm
[RdHi,RdLo]=[RdHi,RdLo]+(Rn*Rm)

## Slide 24: Data Transfer Instructions
Transfer data between memory and processor registers
Single register load/store
Data types supported are signed and unsigned words(32 bits), half word, bytes. Eg.
Multiple register load/store
Transfer multiple registers between memory and the processor in a single instruction
Swap
swaps content of a memory location with the contents of a register. For semaphore implementation. Eg. SWP (B)

## Slide 29: Stack Addressing
Stack:
  last-in-first-out store
  supports simple dynamic memory allocation [i.e., memory allocation where the address to be used to store a data value is not known at the time the program is compiled or assembled]
  Implemented as a linear data structure which
    grows up (an ascending stack) - memory as data is added to it and or
    Grows down (a descending stack) - shrinks back as data is removed
Stack pointer holds the address of the current top of the stack, either by pointing to the last valid data item pushed onto the stack (a full stack), or by pointing to the vacant slot where the next data item will be placed (an empty stack).

## Slide 30
ARM multiple register transfer instructions support all four forms of stack:
  Full ascending: the stack grows up through increasing memory addresses and the base register points to the highest address containing a valid item.
  Empty ascending: the stack grows up through increasing memory addresses and the base register points to the first empty location above the stack.
  Full descending: the stack grows down through decreasing memory addresses and the base register points to the lowest address containing a valid item.
  Empty descending: the stack grows down through decreasing memory addresses and the base register points to the first empty location below the stack.

## Slide 32: Block Copy Addressing
Copy a block of data from one place in memory to another place
Block copy view is based on whether the data is to be stored above or below the address held in the base register and whether the address incrementing or decrementing begins before or after storing the first value.

## Slide 33: Block copy view-Multiple register transfer addressing mode

## Slide 34: Block copy view-Multiple register transfer addressing mode

## Slide 35: Mapping between the stack and block copy views of the load and store multiple instructions

## Slide 36: Copy 8 words from location ro point to location r1 point
LDMIA r0!, {r2-r9}
STMIA r1, {r2-r9}

## Slide 37: If r2 to r9 contains some useful information, it has to be pushed to stack
STMFD r13!, {r2-r9} ; save regs onto stack
LDMIA r0!, {r2-r9}
STMIA r1, {r2-r9}
LDMFD r13!, {r2-r9} ; restore from stack

## Slide 40
Swap between memory and register.
Syntax: SWP {B} {<cond>} Rd, Rm, [Rn]

## Slide 41: Control flow instructions
Determines which instructions next.
  Branch
  Branch Conditions

## Slide 52: Thank You
References:
Text books: ARM System on Chip Architecture, 2nd edition,by Steve Furber ( Chapter 3 & 5)
https://youtu.be/UdY5RkkT7bg?list=PLbRMhDVUMngcJu5oUhgpgYqtOn7DmSfuU
https://youtu.be/yXSTWW0O1LE?list=PLbRMhDVUMngcJu5oUhgpgYqtOn7DmSfuU
https://youtu.be/xYQ60EqTNuo?list=PLbRMhDVUMngcJu5oUhgpgYqtOn7DmSfuU